Overview
This document describes a low-overhead serial communications protocol to be used on microcontroller-based firmware projects that do not otherwise have resources to support other common protocols such as MODBUS. The goals of this protocol are as follows:

- Require minimal resources from the MCU. This includes:
  - Minimal code size
  - RAM usage is flexible per specific application. The entire implementation of the communications stack may be less than 10 RAM bytes.
  - Hardware timers are not required. No accurate timing needed.
- The protocol will be implemented using ASCII encoding. This will allow the use of simple terminal programs to communicate with the device.
- Interpretation of the data is application specific. This allows the protocol to support large or complex data types as well as very small data types when resources such as flash and/or RAM are limited.

It should be noted that this protocol has been designed explicitly for use as a diagnostic tool. This protocol is not designed to be implemented as a primary communications link where errors introduced into the link would result in incorrect functionality of the intended application.

Communication Topology
This is a master / slave protocol. This means that the device designated as the master (typically a computer) would be the only device allowed to initiate a transaction. The slave device would then be expected to respond to the master’s request. This protocol is not designed to be implemented in a multi-drop fashion, that is, there shall only be one master and one slave device on the communications bus.

The suggested communication settings are as follows:
- 19200 Baud Rate
- Even Parity
- 1 Stop Bit

Error Checking
There is no method of checksum error checking inherent in the protocol. This allows a user to easily interface with the device through the use of a simple terminal program. However, checksum protection may be implemented as a specific function (see suggested functions for more information). Parity checking is recommended. It is recommended to use even parity.

General Packet Description
Both request packets (which are sent by the master) and response packets (which are sent by the slave) consist of a series of ASCII characters which are grouped into hexadecimal byte representations of the data. These packets are delimited with special non-alpha-numeric characters.

Request Packet Specification
The request packet is prefixed with a ‘:’ character (0x3A). It is delimited with carriage return (0x0D) and line-feed (0x0A) characters. The packet also consists of a function byte and data-descriptor byte as shown in figure 1.

Request Packet Format
:	Function	Data Descriptor	Data 1	Data 2	...	Data n-1	Data n	CR (0x0D)	LF (0x0A)

Figure 1

The function and data descriptor bytes are single hex byte values represented by two ASCII characters each. For example, if the packet is requesting a function with decimal value 95 (0x5F), then the function field would consist of the ASCII characters 5F. This would be transmitted as two characters (ASCII 5 = 0x35, ASCII F = 0x46). The data descriptor field follows the same format.

An example is presented below in figure 2. In this example, the master is sending a request the following information:

Function Code = 29 (decimal) = 0x1D
Data Descriptor Code = 0 (decimal) = 0x00
Data byte 1 = 100 (decimal) = 0x64
Data byte 2 = 45 (decimal) = 0x2D

Example Request Packet
Field	Start Char	Function	Data Descriptor	Data 1	Data 2	CR	LF
ASCII	:	1D	00	64	2D	CR	LF
HEX	0x3A	0x31;0x44	0x30;0x30	0x36;0x34	0x32;0x43	0x0D	0x0A

Figure 2

Response Packet Specification
The response packet is of the same basic form as that of the request packet. The primary difference if that the starting character is a ‘|’ character (0x7C) instead of a ‘:’ character. The function code and data descriptor fields are echoed from the request packet. Figure 3 shows the basic format of a response packet.

 Response Packet Format
|	Function	Data Descriptor	Data 1	Data 2	...	Data n-1	Data n	CR (0x0D)	LF (0x0A)

Figure 3

An example of a response packet is shown in figure 4. This would be possible response to the request packet in figure 2. In this example, the response data is shown below:
Data byte 1 = 0 (decimal) = 0x00
Data byte 2 = 253 (decimal) = 0xFD

Example Response Packet
Field	Start Char	Function	Data Descriptor	Data 1	Data 2	CR	LF
ASCII	|	1D	00	00	FD	CR	LF
HEX	0x7C	0x31;0x44	0x30;0x30	0x30;0x30	0x46;0x44	0x0D	0x0A

Figure 4

Error Response Packet
If for some reason the slave is unable to process a request, an error packet will be sent. The error response packet is very similar to a normal response packet except that the starting character is a ‘!’ character as opposed to a ‘|’ character. The function code is echoed from the request packet. The data-descriptor shall contain an error code. The error code may be one of the standard codes shown in Figure 6, or the error code can be a application specific code. Figure 5 shows an example of an error response packet. In the example, the error code is 0x00 (unsupported function). In this example, the slave device is telling the master that it does not support function 0x1D.

Error Response Packet
Field	Start Char	Function	Data Descriptor	CR	LF
ASCII	!	1D	00	CR	LF
HEX	0x21	0x31;0x44	0x30;0x30	0x0D	0x0A

Figure 5

Error response codes are returned in the descriptor field. Figure 6 lists supported error codes.

Error Code List
Error Type	Error Description	Error Code
Unsupported Function	The requested function is not supported by the slave device	00
Invalid Data-Descriptor	The data-descriptor is invalid for the specified function	01
Invalid Data	The data in the data fields is invalid or unacceptable	02
Insufficient Rx Buffer Size	The device does not support the size of the request packet.	03
Invalid Character	An invalid ASCII code was received.	04
Invalid Packet length	All packets must have an ODD packet byte count. Function, Data-Descriptor, and Data fields are all 2-byte fields, as is CRLF. The starting packet byte (:, |, or !) makes the packet ODD length.	05
Insufficient Tx Buffer Size	The device does not support the size of the response packet.	06
Reserved	Do not use these error codes, reserved for future use.	06 – 7F
Application Specific	These codes are specific to the particular application.	80 - FE
Extended Error Code	The error code is represented with multiple bytes in the data field. This is application-specific by definition.	FF

Figure 6

Packet Transaction Procedure
All transactions are initiated by a request from the master. The master will expect a response packet from the slave device within a certain timeout period. The response timeout period is defined to be the period of time between the start of the linefeed character transmission and the reception of the response packet’s starting character. The standard response timeout period for a device is suggested to be 5 seconds; however, this may be adjusted to suit the specific application.

Because this protocol is designed to work with both full and half-duplex communication links, the slave device will not respond to incomplete packets. This will help prevent data collisions in half-duplex mode.

Figure 7 shows a state machine table which implements the protocol from the perspective of a slave device. Figure 8 describes basic slave behavior for each state.

Slave State Diagram
Current State	State Changing Event	Next State
STARTUP	N/A	WAIT_FOR_START_CHAR
WAIT_FOR_START_CHAR	Receive ‘:’ character	RECEIVING_PACKET
RECEIVING_PACKET	Receive ASCII carriage return	WAIT_FOR_LINEFEED
	Parity or Framing error detected	WAIT_FOR_START_CHAR
WAIT_FOR_LINEFEED	Receive ASCII Linefeed character	PROCESS_PACKET
	Receive any character other than LF	WAIT_FOR_START_CHAR
PROCESS_PACKET	N/A	SEND_RESPONSE
SEND_RESPONSE	Last byte of response (LF character)is transmitted	WAIT_FOR_START_CHAR

Figure 7

Description of States
State Name	Description
STARTUP	This is a pass-through state which initializes the system and sets the state machine to WAIT_FOR_START_CHAR. This state may actually be implemented outside of the state machine as a separate process/function.
WAIT_FOR_START_CHAR	In this state the slave device is waiting for an incoming start character from the master.
RECEIVING_PACKET	In this state the slave places any received characters into a buffer which will eventually hold the entire received packet. If a ‘:’ character is received, the buffer is cleared and the slave device remains in this state.
WAIT_FOR_LINEFEED	The slave has just received a CR character, and is now waiting for the LF character.
PROCESS_PACKET	The packet is considered complete and is parsed. A response is packet is constructed.
SEND_RESPONSE	The response packet is being sent to the master.

Figure 8

Specified Functions and Data Descriptors
This section describes a few common functions and data descriptors that are commonly used among many applications. None of the functions or data descriptors listed below are required to be implemented in a specific application except for function 0x00 (Diagnostic Echo).

Diagnostic Echo
Read Data Register
Write Data Register
Read Data Register w/ Checksum
Write Data Register w/ Checksum

Diagnostic Echo (0x00)
The diagnostic echo function is required to be implemented with the protocol because it takes virtually no code space to implement and is a very quick way to verify a successful communication link between master and slave.

An example is presented below in figure 9. In this example, the master is sending a request for a diagnostic echo of some arbitrary data (in this case, the data happens to represent the bytes 0x12 and 0x34). All data following the function code 0x00 shall be echoed so long as the packet does not overflow the data buffer. Please note that the data descriptor field is treated like an ordinary 1-byte data field for this function.

Function Code = 0 (decimal) = 0x00
Data Descriptor Code = 18 (decimal) = 0x12
Data byte 1 = 52 (decimal) = 0x34

Example Diagnostic Echo Request Packet
Field	Start Char	Function	Data Descriptor	Data 1	CR	LF
ASCII	:	00	12	34	CR	LF
HEX	0x3A	0x30;0x30	0x31;0x32	0x33;0x34	0x0D	0x0A

Figure 9

The slave shall reply with the data shown in figure 10.

Example Diagnostic Echo Response Packet
Field	Start Char	Function	Data Descriptor	Data 1	CR	LF
ASCII	:	00	12	34	CR	LF
HEX	0x3A	0x30;0x30	0x31;0x32	0x33;0x34	0x0D	0x0A

Figure 10

Read Data Register (0x01)
The Read Data Register function allows the master to read data which has been mapped to a given register. The mapping of data to registers is application specific.

Figure 10 shows suggested data descriptors for specific data types.
Data Type	Description	Data Descriptor
UINT8	Unsigned 8-bit integer (BYTE)	0x00
INT8	Signed 8-bit integer	0x01
UINT16	Unsigned 16-bit integer	0x02
INT16	Signed 16-bit integer	0x03
UINT32	Unsigned 32-bit integer	0x04
INT32	Signed 32-bit integer	0x05
FLOAT	32-bit floating-point number (single)	0x06

Figure 10

An example is presented below in figure 10. In this example, the master is sending a request to read register 3 of a byte data type (in this case, the data reported by the slave happens to be 129).

Function Code = 1 (decimal) = 0x01
Data Descriptor Code = 0 (decimal) = 0x00
Data Field 1 (High Byte of Register) = 0x00
Data Field 2 (Low Byte of Register) = 0x03

Example Diagnostic Echo Request Packet
Field	Start Char	Function	Data Descriptor	Data 1	Data 2	CR	LF
ASCII	:	01	00	00	03	CR	LF
HEX	0x3A	0x30;0x31	0x30;0x30	0x30;0x30	0x30;0x33	0x0D	0x0A

Figure 9

The slave shall reply with the data shown in figure 10.

Example Diagnostic Echo Response Packet
Field	Start Char	Function	Data Descriptor	Data 1	CR	LF
ASCII	:	00	12	34	CR	LF
HEX	0x3A	0x30;0x30	0x31;0x32	0x33;0x34	0x0D	0x0A

Figure 10

Read Data Register with Checksum Protection (0x03)
The Read Data Register function allows the master to read data which has been mapped to a given register. This function is very similar to function 0x01 with the addition of a 16-bit CRC checksum word appended to the data. This allows for assurance of data correctness. The mapping of data to registers is application specific.

Figure 10 shows suggested data descriptors for specific data types.
Data Type	Description	Data Descriptor
UINT8	Unsigned 8-bit integer (BYTE)	0x00
INT8	Signed 8-bit integer	0x01
UINT16	Unsigned 16-bit integer	0x02
INT16	Signed 16-bit integer	0x03
UINT32	Unsigned 32-bit integer	0x04
INT32	Signed 32-bit integer	0x05
FLOAT	32-bit floating-point number (single)	0x06

Figure 10

An example is presented below in figure 10. In this example, the master is sending a request to read register 3 of a byte data type (in this case, the data reported by the slave happens to be 129).

Function Code = 1 (decimal) = 0x01
Data Descriptor Code = 0 (decimal) = 0x00
Data Field 1 (High Byte of Register) = 0x00
Data Field 2 (Low Byte of Register) = 0x03

Example Diagnostic Echo Request Packet
Field	Start Char	Function	Data Descriptor	Data 1	Data 2	CR	LF
ASCII	:	01	00	00	03	CR	LF
HEX	0x3A	0x30;0x31	0x30;0x30	0x30;0x30	0x30;0x33	0x0D	0x0A

Figure 9

The slave shall reply with the data shown in figure 10.

Example Diagnostic Echo Response Packet
Field	Start Char	Function	Data Descriptor	Data 1	Hi CRC	Lo CRC	CR	LF
ASCII	:	00	12	34	E3	7E	CR	LF
HEX	0x3A	0x30;0x30	0x31;0x32	0x33;0x34		0x37;0x4	0x0D	0x0A

Figure 10

END OF DOCUMENT